## Slide 1: Install and Configure CPUs
Lesson 2
Topic 2D
Notes: This topic concludes the review of the main hardware components.

## Slide 2: CPU Architecture
CPU pipeline
  Fetch, decode, execute, writeback
  Registers and cache
x86 CPU architecture
  32-bit IBM PC-compatible instruction set
x64 CPU architecture
Advanced RISC Machines (ARM) CPU architecture
  System-on-a-chip
  Better power and thermal efficiency
  Software compatibility and emulation
Notes: Re-cap the role of the CPU in processing low-level instructions and use of registers and cache. Explain how the instruction set and width (32-bit or 64-bit) determines software compatibility with hardware. Contrast ARM with x86/x64.

## Slide 3: CPU Features
Clock speed
Multithreading
  Simultaneous multithreading (SMT)/HyperThreading
  Requires software support
Symmetric multiprocessing (SMP)
  Requires multiple CPUs and sockets
  CPUs must be identical models and specifications
Single core versus multi-core
Virtualization support

## Slide 4: CPU Socket Types
© Gigabyte Technology
Intel | AMD
Socket form factor Zero insertion force (ZIF) Land grid array (LGA) Predominantly Intel socket form factors Pins on the motherboard | Pin grid array (PGA) Predominantly AMD socket form factors Pins on the CPU package
Notes: Make sure students can distinguish these socket types. If you have some old examples to show or provide as hands-on that will boost students’ understanding. Discuss some of the mechanics of removing and installing CPUs.

## Slide 5: Lab Activity
Virtual Workbench Lab: Install a CPU and Cooler